## Slide 1: TRICS Guidance Note: Practical Implementation of the Decide and Provide Approach Lynn Basford BasfordPowers Ltd Glenn Lyons UWE / Mott MacDonald

## Slide 2: Purpose of the presentation
To set out the guidance.
Show the journey of developing the Decide and Provide Principles.
Set out what is the Decide and Provide Process and its component parts.
How to use TRICS and the Decide and Provide.

## Slide 3: Scene setting

## Slide 4: Changing travel behaviour
Would you tell me, please, which way I ought to go from here?

## Slide 5: What change we have seen

## Slide 6: It’s the need for access, stupid
Spatial Proximity
Digital Connectivity
Accessibility
Physical Mobility
Land Use System
Transport System
Telecommunications
System
“Transport does not merely serve society: it shapes society, as in turn society shapes transport”
(Lyons, 2004)

## Slide 7: A state of flux and a need for change
Global shock
Preferred future

## Slide 8: From predict and provide to decide and provide
Predict and provide – forecast a most likely mobility future (within sensitivity-tested bounds of uncertainty) and provide a means to accommodate projected demand
demand-led supply ● reactive
Decide and provide – decide on a preferred accessibility future (and outcomes) and provide a means to move towards it in a way that accommodates the deep uncertainty ahead
supply-led demand ● proactive

## Slide 9: TRICS – it’s how you use it that matters
TRICS data depict the past, not the future
The past and future can be interpreted differently
Remember that any attempt to project future trip rates is a judgement based upon assumptions

## Slide 10: Guidance Note

## Slide 11: Purpose
To inform plan making and related strategic land use and transport planning
To support and assist the practical implementation of the Decide and Provide Approach in the preparation, and review of transport appraisals, including Transport Assessment and Transport Statements
To maximise the use of TRICS’s bank of survey data to best effect
To address the lack of guidance in this area and,
To support and reflect the ongoing paradigm shift
The Guidance challenges orthodox wisdom and practices

## Slide 12: What is the Decide and Provide approach?
Decide and Provide is to:
  Decide on the preferred future and provide the means to work towards that which can accommodate uncertainty.
  It allows us to:
  Adopt a more positive and integrated transport and land use planning approach
  Achieve more meaningful implementation of a modal hierarchy that prioritises walking and cycling
  Better support the decarbonisation of transport

## Slide 13: What is the Decide and Provide approach?
Decide and Provide involves:
  Visioning
  Acknowledging deep uncertainty
  Scenario Planning
  Understanding the quantum, scale and mix of proposed development
  Using trends and historic trend data

## Slide 14: Visioning

## Slide 15: What is the approach?
Visioning:
  Central to place making and creating better places to live, work and play (shaping not serving)
  Three overarching key questions for visioning are:
    What sort of place are we creating?
    What kind of activities do we need or desire to travel for?
    How will we provide for mobility?
    Transport planners need to understand, influence and share the vision that land use planners have for a place (for a plan) or for a specific site (for a project)

## Slide 16: Probing for better planning
What can the ratio of new homes and new jobs be? (taking into account proximity and provision)
What can the provision of local retail and community services be ?
What can the work from home provision, including broadband infrastructure be?
What can the relationship to existing education services and/or the provision of new educational facilities be?
What can the active travel provision, including the provision of new (or upgrade of existing) pedestrian and cycle infrastructure be ?

## Slide 17: Scenario Planning

## Slide 18: What is scenario planning?
Scenarios make you think
https://doi.org/10.1016/j.trip.2021.100438

## Slide 19: How many scenarios do you need?
The number of scenarios needed will be a matter of professional judgement.
This Guidance suggests that three different and plausible scenarios typically be considered.

## Slide 20: Acknowledging deep uncertainty in making your case

## Slide 21: Acknowledging uncertainty in making your case
Increasing acknowledgement of deep uncertainty:
  Changes in consumer behaviour lead to uncertainty
  Pandemic and other interruptors
  Need to state what uncertainty has been taken into account in assessing development impacts
  Use evidence; trends and historic trend data to reflect and report on uncertainties.
  Adds resilience to decision making
  Make the case for the design of the settlement to be resilient.
  HAVE YOU ACKNOWLEDGED UNCERTAINTY?

## Slide 22: A Deep Dive for the TRICS User

## Slide 23: Using TRICS Database to Decide and Provide
TRICS Database contains survey data going back to the beginning of the 1990’s
Multi-modal data collected since January 2000
The survey data is a record of travel behaviour for each site on the day of survey
Myth – “TRICS promotes Predict and Provide culture”
  The database is a record of survey information.
  It’s the way people choose to use this data which is important.
  Changing the way the information is used can promote Decide and Provide.

## Slide 24: Historic trends
Decide and Provide acknowledges what has happened in the past and uses trend information to inform the future.
The number of surveys within TRICS allows analysis of surveys to be filtered and output so they can be used to display historic trends.
TRICS has suggested a procedure to undertake this, which follows the recommendations within the Decide and Provide Guidance Note.
Excel Historic Trend Template available from http://www.trics.org/decideandprovideguidance.html

## Slide 25: Historic trends
Notes of explanation for Graph:
VO – Data obtained from Vehicle Only data
MM – Data obtained from Multi-Modal Data
PFS – Petrol Filling Station
Data within the graph is obtained from multiple TRICS sites, all within the same parameters set by the user. Each time slice will contain a different mixture of sites that all meet the defined parameters.

## Slide 26: Historic trends analysis
Working left to right:
1st Filtering screen – Firstly analyse/calculate for all Vehicle Only segments then all Multi-Modal segments.
2nd Filtering screen – select your Primary Filters that replicate your site and then change the date range at the bottom to reflect your timeslice requirements, work to 5 year intervals, but if you have a good sample size this could be reduced to 4 years or even smaller if required. Keep filtering parameters the same for EVERY calculation undertaken for that trend analysis. Use of the TRICS Good Practice Guide should be followed in relation to site selection, as you would for a usual TRICS analysis. 2021 Good Practice Guide

## Slide 27: Historic trends analysis

## Slide 28: Historic trends Excel template
Green Area for users to keep notes on Parameters used during TRICS Analysis
Due to Multi-Modal data only starting in 2000 you note that we will have no data for these Travel Modes for the first 2 time slices
Data from CSV file then copied into relevant Timeslice TAB within Excel
If output correctly, as outlined within the Instructions Page, all data should be in correct format and in the correct order for plotting to a Graph

## Slide 29: Historic trend analysis
The Trends Output page can then be used to view different information by changing the drop down boxes highlighted yellow.
The first 2 yellow boxes enable the user to select a time period anything from 1 hours to the complete day.
The third box allows the user to select Arrivals, Departures or Totals
There are 4 graphs available for the display of data within the Template, but more can be easily added if you are competent with Excel formula
You can then copy and paste the information from this page into your Word documents as required.

## Slide 30: Decide & Provide doesn’t stop at construction
Monitoring is an extremely important element of the D&P process. As Transport Professionals how do we know what is working and what is not?
How many of you have been back to a site you were involved with 10 years ago to physically record the Travel Behaviours, to see if your assumptions were correct?
We need to ensure that every £ spent on constructing a development is value for money and worthwhile for the local population.
Without proper independent monitoring we could all be following the wrong path and making things worse, or at best, not improving them as much as we thought.
The use of TRICS SAM process can support and strengthen the Monitoring and Evaluation Plan. Independent monitoring surveys with the provision of standardised, unbiased survey data that adds to the evidentiary base.

## Slide 31: The Decide and Provide journey continues…
August 2021
https://www.itf-oecd.org/travel-transitions-policy-makers-respond-mobility-trends
https://www.tapforuncertainty.eu/
May 2021 – April 2024